## Slide 1: RTC on the Teensy 3.6
WEA
2017-12-15

## Slide 2: Summary
Goal:
  Make RTC work on the Teensy so that Tympan users can maybe log time-based data across many different use sessions
Problem:
  The Teensy looses the time whenever power is cut to the Teensy (such as via the power switch)
Solution Approach:
  Design a connection directly from the LiPo battery to power just the Teensy’s RTC
Result:
  Used a voltage divider (50K/125K). Installed on a Tympan Rev A
  Used the Teensy Time library (I didn’t have to write any code!)
  It works!
This doc:
  Shows the mods that I did. Discusses how the RTC works. Shows calcs for resistor divider.

## Slide 3: Connect to LiPo Somewhere between the Battery and the Power Switch
Grab VLiPo Between Battery and Switch
Grab Ground Anywhere on the PCB

## Slide 4: Add Voltage Divider from LiPo to Supply RTC VBat
View from Below Teensy
View from Above Teensy
Vbat
J1
J2
D7
D6
IN3
Line-O
+
G
L
R
L
R
OFF
ON
J5
R19
U2
U23
U24
D5
D10
D11
Mic
R
Mic
L
TYMPAN
J6
Connect to underside of board?
R1
+
Gnd
TP2 is also Gnd,
If you prefer
R2
R1=50K
R2=125K
CoolAid, 2017-12-15, WEA

## Slide 5
J1
J2
D7
D6
IN3
Line-O
+
G
L
R
L
R
OFF
ON
J5
R19
U2
U23
U24
D5
D10
D11
Mic
R
Mic
L
TYMPAN
LiPo
Via F1
Gnd
Via TP2
125K
50K
RTC VBat
On Teensy
Battery +
(on F1)
Ground
(on TP2)
R2 = 125K
R1 = 50K
RTC VBat
Hole

## Slide 6: Modification to Tympan Rev A
Battery +
(on F1)
Ground
(on TP2)
R2 = 125K
R1 = 50K
RTC Vbat
Hole

## Slide 7: Fits in Enclosure!

## Slide 8: Testing – It works!
Used Teensy Example “TimeTeensy3” from the Time library that can be installed with Teensyduino
Using an unmodified Teensy, time keeps getting lost
  Time is kept correctly until you turn off the Tympan power switch. When you turn it back on, time is reset back to the beginning.
Using my modified Teensy, time is kept correctly
  Correct time is maintained despite turning power switch off/on
  Correct time is maintained despite plugging/unplugging from USB

## Slide 11: How RTC on the Teensy Works
Teensy 3.6 has an oscillator and counter that keep running, as long power is applied to Vbat
  Upon first power up, it starts counting from zero
  If you know what time it was at count = zero, then you know what time it is now.
  As long as power to Vbat is maintained, it keeps a continuous count.
Vbat is internally connected to the main power supply so that, whenever the Teensy itself is powered, the RTC counts correctly
  The trick is what happens when power is removed from the Teensy. Normally it would lose count.
  Typically, one wires a coin cell to the RTC’s Vbat to supply power when the Teensy itself is unpowered
  As long as the coin cell keeps its voltage, the RTC never loses count. Time is maintained.
  Instead, we have wired in our LiPo Battery instead.
To access the RTC count, the Teensy folks wrote a Time library
  It takes care of all the back-end how to access and interpret the RTC_count
  It presents a human-readable date/time to the user based on some reference time that corresponds to RTC_Count = zero.
Where does the Time library get the reference time/date?
  When the Teensy sketch is compiled, the compiling of the Time library poles the PC’s current time/date
  This value is tored in the Flash on the Teensy. This becomes the reference time for the RTC count = zero.
Key implications:
  If power is maintained to Vbat, the RTC counter keeps accumulating and time is correct
  If power is lost to Vbat, the count is lost. When power is re-applied, the counter restarts. Since it thinks that counter = zero is the reference time stored in flash, the user is told the wrong time/date.
Unknowns:
  It is unclear to me whether the system *knows* if power has been lost or not. This seems like an important thing to be aware of. More experimentation is needed.

## Slide 12: Voltage Divider Calcs
See Discussion on Teensy Forum: https://forum.pjrc.com/threads/48417-Voltage-limit-on-Teensy-3-6-for-RTC-Vbat
Resistor
Values
Vbat is low enough. Good.
Available current to RTC is up to 0.028 mA.
Hopefully this is good enough